## Slide 1
MCA MAJOR PROJECT
OpenCV-Based System for Crack Identification and Width Estimation
PATEL MAN VISHNUBHAI
Enrollment No. 25IC03CA053
Guide: Dr. Srikant Singh
School of Engineering, P P Savani University
Notes: Introduce the project: a web application that finds cracks in photos and measures their length and width using classical computer vision.

## Slide 2: Contents
1
Project Overview
2
Technology & Design
3
Processing Pipeline
4
The Nine Models
5
Database
6
Implementation
7
Testing & Results
8
Wrap-up
Notes: Eight parts. The slide numbers show where each part starts.

## Slide 3: Project Overview
What the system is and why
01
Notes: Part one: the idea.

## Slide 4: Project at a glance
Item | Detail
Name | Crack Identification and Width Estimation
Purpose | Find cracks, measure length and width, grade severity
Surfaces | Concrete, asphalt, roads, walls
Front end | HTML5, Bootstrap 5, JavaScript
Back end | Python, Flask, OpenCV, NumPy, scikit-image
Database | MongoDB (in-memory fallback)
Notes: Summary of the project from the project details file.

## Slide 5: Cracks are early warning signs
Slow
Manual gauge and tape
Subjective
Differs by inspector
Poorly recorded
Little visual evidence
Notes: Inspection is slow, subjective and poorly recorded.

## Slide 6: Objectives
Upload images
Find cracks
Reject non-cracks
Length and width
Convert to mm
Export reports
Keep history
Notes: Seven objectives from upload to history.

## Slide 7: Which model is used?
Classical computer vision + rule-based classifier
Fast
CPU only
Explainable
Exact geometry
No training data
Works directly
Calibrated
Pixels to mm
Notes: No neural network and no GPU. A classical computer-vision pipeline plus a rule-based severity classifier.

## Slide 8: Classical vs deep learning
 | Deep learning | This project
Training data | Large labelled set | None needed
Hardware | GPU | Ordinary CPU
Explainable | Black box | Every stage visible
Width in mm | Not directly | Yes, with scale
Unseen textures | Stronger | Weaker
Notes: Trade-off: classical is transparent and light, deep learning is stronger on unseen textures.

## Slide 9: Technology & Design
Tools and architecture
02
Notes: Part two.

## Slide 10: Technology stack
Component | Technology | Role
Language | Python 3.10+ | Whole back end
Web framework | Flask 3 | Routes, controllers
Computer vision | OpenCV 4.9+ | Image processing
Numerical | NumPy | Matrix maths
Morphology | scikit-image | Skeletonization
Database | MongoDB / Mongomock | Records, fallback
Reports | ReportLab, pandas | PDF and CSV
Front end | Bootstrap 5.3 | Responsive UI
Notes: All open source.

## Slide 11: Technology at a glance
Python
Language
OpenCV
Images
scikit-image
Skeleton
Flask
Web server
MongoDB
Storage
ReportLab
PDF reports
Notes: Six main building blocks.

## Slide 12: Layered architecture
Presentation
HTML pages, JS
Application
Flask routes
Processing
OpenCV services
Data
MongoDB + files
Notes: Presentation, application, processing and data layers.

## Slide 13: How a user works with it
Upload
Choose photos
Analyse
Automatic
Review
Images and numbers
Export
CSV, PDF, ZIP
Notes: Upload, analyse, review, export.

## Slide 14: Data flow and use cases
Use cases
Notes: Level-1 data flow diagram and the use-case diagram.

## Slide 15: Processing Pipeline
Eleven steps from photo to result
03
Notes: Part three.

## Slide 16: Pipeline overview
1
Resize
max 1600 px
2
Grayscale + blur
5×5 Gaussian
3
CLAHE
local contrast
4
Black-Hat
dark valleys
5
Adaptive threshold
41×41 window
6
Clean + bridge
close gaps
7
Geometry filter
SVD ratio ≥ 3
8
Unify paths
link nearby parts
9
Skeleton
1 px centre line
10
Width
distance transform
11
Calibrate + draw
mm, annotate
Notes: Eleven steps. Each saves an image so it can be checked.

## Slide 17: Steps 1 to 6: prepare the image
Step | What happens | Setting
1 Resize | Scale down large photos | max 1600 px
2 Grayscale + blur | One channel, less noise | Gaussian 5×5
3 CLAHE | Even out shadows | clip 2.0, 8×8 tiles
4 Black-Hat | Show dark narrow lines | ellipse 21×21
5 Adaptive threshold | Crack pixels = white | 41×41 window
6 Clean + bridge | Fill gaps, drop specks | min area 30 px
Notes: Resize, remove noise, boost contrast, highlight dark lines, threshold and clean.

## Slide 18: Steps 7 to 11: measure the crack
Step | What happens | Setting
7 Geometry filter | Reject round blobs | ratio ≥ 3.0
8 Unify paths | Join nearby pieces | link distance 25 px
9 Skeleton | Centre line = length | scikit-image
10 Width | Distance to the edge | 2 × radius
11 Calibrate + draw | Pixels to mm, annotate | 10 px = 1 mm
Notes: Filter shapes, join pieces, thin to a line, measure width, convert to mm.

## Slide 19: Every stage is saved as an image
Notes: These are the real images produced by the application for one synthetic crack.

## Slide 20: Threshold: crack becomes white
Grayscale
After threshold
Notes: The adaptive threshold adapts to uneven light.

## Slide 21: Clean up and keep crack shapes
Threshold
Cleaned
Crack mask
Rule | Value
Smallest piece kept | 30 px
Long and thin (ratio) | ≥ 3.0
Notes: Specks are removed, then only long thin shapes are kept.

## Slide 22: Images with no crack are rejected
Test image | Result
Plain wall | Rejected
Round blob | Rejected
Text image | Rejected
Texture only | Rejected
Crack image | Accepted
4 of 4
non-crack images rejected
Notes: Four non-crack images were tested; all were rejected.

## Slide 23: The Nine Models
Methods used inside the pipeline
04
Notes: Part four.

## Slide 24: Nine models at a glance
No | Model | Job
1 | CLAHE enhancement | Even out light
2 | Black-Hat morphology | Find dark thin lines
3 | Adaptive Gaussian threshold | Crack vs background
4 | Morphological closing | Bridge small gaps
5 | Component linking graph | Join one crack
6 | SVD geometric filter | Reject round blobs
7 | Skeletonization | Length
8 | Distance transform | Width
9 | Rule-based severity | Good / Medium / Heavy
Notes: Nine methods, each with one clear job.

## Slide 25: Models 1 to 3: find the crack
1
CLAHE
clip 2.0, 8×8 tiles
Evens out shadows and lighting
2
Black-Hat
closing − image, 21×21
Isolates narrow dark lines
3
Adaptive threshold
41×41 Gaussian window
Handles uneven lighting
Notes: Enhance contrast, isolate dark lines, then threshold locally.

## Slide 26: Models 4 to 6: clean and verify
4
Gap bridging
morphological closing
Joins cracks broken by stones
5
Component linking
link distance 25 px
Merges pieces into one crack
6
SVD filter
ratio σ1 / σ2 ≥ 3
Rejects gravel and pits
Notes: Close gaps, link pieces, reject blobs by shape.

## Slide 27: Models 7 to 9: measure and grade
7
Skeletonization
scikit-image skeletonize
One-pixel centre line gives length
8
Distance transform
width = 2 × radius
Median = mean width, P95 = max
9
Severity rules
Good, Medium, Heavy
Compares width with thresholds
Notes: Skeleton for length, distance transform for width, rules for severity.

## Slide 28: Skeleton and distance transform
Skeleton
Distance transform
Width samples
609.6 px
crack length (60.96 mm)
7.19 px
mean width (0.72 mm)
8.00 px
maximum width (0.80 mm)
Notes: The skeleton is a one-pixel centre line; the distance transform gives the radius to the edge.

## Slide 29: Worked example: a 5 px bar
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1
1 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 2 | 1
1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Distance values across the bar (centre row highlighted)
width = 2 × distance
2 × 3.0 = 6.0 px
true bar width: 5 px
Notes: Distance values rise to 3 at the centre, so width = 2 × 3.0 = 6.0 px, one pixel above the true 5 px.

## Slide 30: Measurements and units
Measure | How | Unit
Length | Sum of skeleton links | px and mm
Mean width | Median of 2 × radius | px and mm
Maximum width | 95th percentile | px and mm
Area | Crack pixels | px² and mm²
Scale | Default 10 px = 1 mm | px per mm
Notes: Length sums skeleton links, widths use median and 95th percentile, mm = px divided by pixels-per-mm.

## Slide 31: Severity: Good, Medium, Heavy
Good
≤ 3 px
≤ 0.30 mm
Medium
3 – 8 px
0.30 – 0.80 mm
Heavy
> 8 px
> 0.80 mm or area ≥ 5000 px²
Notes: Software label based on mean width and area. It is not a structural safety verdict.

## Slide 32: Database
Three collections
05
Notes: Part five.

## Slide 33: Three collections
Analysis
One upload batch
Image
One photo
Measurement
One crack
If MongoDB is offline the app keeps records in memory, so it still works.
Notes: Analyses contain images; images contain cracks.

## Slide 34: Analysis collection
Field | Meaning
analysis_id | Unique id of the session
status | Uploaded, Processing, Completed, Failed
total_images | Images in the batch
total_detected_regions | Cracks found in the batch
pixels_per_mm | Scale, default 10
severity_thresholds | Good / Medium / Heavy limits
Notes: Key fields of the analysis record.

## Slide 35: Image collection
Field | Meaning
image_id | Unique id of the image
analysis_id | Link to the batch
original_filename | Name of the uploaded file
resize_scale | Scale applied on load
workflow_times | Time per step in seconds
processed_paths | Paths of all stage images
Notes: Key fields of the image record.

## Slide 36: Measurement collection
Field | Meaning
crack_id | Id of the crack
skeleton_length_px / mm | Centre-line length
mean_width_px / mm | Median width
max_width_px / mm | 95th percentile width
contour_area_px / mm2 | Crack area
severity | Good, Medium or Heavy
Notes: Key fields of one crack record.

## Slide 37: Entity relationship diagram
Notes: Analysis has many images; each image has many cracks.

## Slide 38: Implementation
Project layout and user interface
06
Notes: Part six.

## Slide 39: Project folders
Folder | Holds
models/ | Database and record handling
routes/ | Web page and download endpoints
services/ | Image processing and reports
templates/ | HTML pages
static/ | CSS and JavaScript
tests/ | Automated tests
storage/ | Uploaded and result files
Notes: Each folder has one responsibility.

## Slide 40: The services folder
File | Job
preprocessing_service | CLAHE, blur, Black-Hat, threshold
detection_service | Find, filter and link cracks
measurement_service | Skeleton, width, length
calibration_service | Pixels to millimetres
classification_service | Good / Medium / Heavy
csv, pdf, zip service | Report export
Notes: The services folder contains the processing logic.

## Slide 41: Code size by folder
Chart: Lines of code per folder
| services | routes | tests | top level | models | static | templates | utils
Lines | 786 | 344 | 260 | 180 | 158 | 145 | 59 | 37
Notes: About 1,990 lines in total.

## Slide 42: Two main pages
Page | Address | Use
Upload | /upload | Start a new analysis
History | /history | Open past inspections
Results | /analysis/<id> | Images, table, downloads
Notes: Upload to start, History to revisit.

## Slide 43: Upload page and results page
Upload
Results summary
Notes: Screenshots use synthetic test images.

## Slide 44: Results page: image by image
Original + annotated
Final crack mask
All stage images
Time per stage
Notes: Each image shows the original, the annotated result, the mask and every stage.

## Slide 45: Reports: CSV, PDF, ZIP
34
CSV columns
33
PDF pages
35
files in ZIP
Notes: A two-image test produced a 34-column CSV, a 33-page PDF and a ZIP of 35 files.

## Slide 46: How to run
Option A
Double-click run_crackscope.bat
Option B
Activate the environment, run python app.py
Open
http://127.0.0.1:5000
Test
Run pytest
Notes: Two ways to start the application.

## Slide 47: Testing & Results
What was measured
07
Notes: Part seven. All numbers come from running the code on synthetic images.

## Slide 48: Testing summary
Chart: 22 test cases
| Automated tests | Browser + exports | Experiments
Tests | 16 | 4 | 2
16 / 16
automated tests passed
4 / 4
non-crack images rejected
0.16 s
per 1600 × 1200 image
Notes: 16 automated tests passed; four more checks covered the browser flow and exports; two experiments.

## Slide 49: Width accuracy
Chart: Measured vs true width
| 3 | 5 | 7 | 9 | 11 | 13
Ideal | 3 | 5 | 7 | 9 | 11 | 13
Measured mean width | 2.8 | 5.6 | 7.19 | 8.79 | 10.79 | 12.79
Maximum width (P95) | 4 | 6 | 8 | 10 | 12 | 14
±0.6 px
mean width error
−7 to +12 %
relative error
Notes: Bars of known width on a noisy background; the measured mean follows the true width.

## Slide 50: Error for each width
Chart: Mean-width error by test (teal = narrower, red = wider)
| 3 px | 5 px | 5 px | 7 px | 7 px | 9 px | 11 px | 13 px
Error (px) | -0.2 | 0.6 | 0.6 | 0.19 | 0.19 | -0.21 | -0.21 | -0.21
Notes: Largest error +0.6 px; thin bars have the largest relative error.

## Slide 51: Faint cracks are missed
Chart: Detected crack length vs contrast
| 15 | 25 | 35 | 50 | 70 | 95 | 130
Detected length (px) | 0 | 0 | 609.6 | 609.6 | 609.6 | 609.6 | 609.6
≥ 35
grey levels needed
5 / 5
detected at every noise level
Notes: Below about 30 grey levels of contrast nothing is detected; above that the length is correct.

## Slide 52: Length error depends on angle
Chart: Length error (%) by angle
| 0° | 15° | 30° | 45° | 60° | 75° | 90°
Length error (%) | -1 | 6.8 | 7.1 | -0.4 | 6.4 | 6.2 | -1.2
+6–7 %
at oblique angles
≈ −1 %
at 0°, 45°, 90°
Notes: At 0, 45 and 90 degrees accurate; elsewhere 6 to 7 percent too long. Known limitation.

## Slide 53: Speed
Chart: Seconds per image
| 640 × 480 | 1024 × 768 | 1600 × 1200
Seconds | 0.031 | 0.079 | 0.157
Chart: Time by stage (1024 × 768)
| Pre-processing | Detection | Measurement
Stage | 0.0208 | 0.0168 | 0.057
Notes: Measurement is the largest share of the time.

## Slide 54: Result on a test image
609.6 px
length = 60.96 mm
7.19 px
mean width = 0.72 mm
Medium
severity label
Notes: Input, annotated result, skeleton and width image.

## Slide 55: Wrap-up
Limits, future work, conclusion
08
Notes: Part eight.

## Slide 56: Known limitations
Limitation | Detail
Synthetic tests only | No real-photo benchmark yet
Fixed scale | 10 px = 1 mm, not resize-aware
Faint cracks | Missed under ~30 grey levels
Oblique length | +6–7 % too long
No login | For local use only
Notes: Evidence is synthetic, scale is fixed, faint cracks are missed, no login.

## Slide 57: Future scope
Real datasets
Fix length
Per-image scale
Hybrid model
Deploy
Notes: Real datasets, length fix, per-image scale, hybrid model, deployment.

## Slide 58: Conclusion
0.6 px
width accuracy (synthetic)
< 0.2 s
per 1600 × 1200 image
16 / 16
automated tests passed
Detects and measures cracks
Every stage is visible
CSV, PDF and ZIP reports
Notes: Detects and measures cracks with no training data, shows every stage, exports reports.

## Slide 59
Thank you
Questions?
PATEL MAN VISHNUBHAI · 25IC03CA053
Notes: Thank the audience and invite questions.